## Slide 1: ECE 540 Final Project Team Progress Report
Binata Bhattacharyya
Brian Dharmanto
Chad Klingbeil
Neil Roberts

## Slide 2
Team Members and Ownership
Binata Bhattacharyya VGA Graphics
Brian Dharmanto Verilog Modules
Chad Klingbeil BOT Instructions
Neil Roberts CPU Instructions
Scripting
*NOTE: All team members taking a dynamic role in the development of each area

## Slide 3
Expand Project 2 Capabilities
GOAL: Create Driver’s Viewpoint of RojoBot
Enhance Video & Graphics
Screen to show driver’s viewpoint of map
Pseudo-3D imagery to reflect distance of objects
Use RESERVED map setting for trees
Extend BotSim2.0 sensing capabilities to support new requirements
Add long-distance sensors for obstacle-to-display (O2D) imaging
Enhance CPU ROM Instructions to support off-black-line operations
Allow user interaction with push button control when requested, otherwise autonomous control

## Slide 5
BOT Instructions Added single long-range sensor (LRProxL, LRProxR) to identify objects that will be display on screen
Defined sensor requirements:
Sensors to detect obstacles at two cells and beyond
  Begin with 4 cells deep (2 bits) Cells 2 – 5 visible
  Step to 8 cells deep (3 bits) Cells 2 – 9 visible
  Up to 16 cells deep (4 bits) Cells 2 – 17 visible
Long-range sensor register configuration:
7 6 5 4 3 2 1 0
LProxL LProxR

## Slide 6
BOT Instructions Next Steps
Long-Range Sensor Issue
Insufficient data in a single sensor register for 12 locations containing 1 of 4 possible values
Expand number of long-range sensors to detect objects individually per lane
LRLeft / LRCent / LRRight
  Each sensor to detect objects per lane
  Each sensor register to contain object type and distance
  2 bits to define location (distance)
  2 bits to define object (type: space, black line, obstacle, tree)
7 6 5 4 3 2 1 0
Type RESERVED Distance

## Slide 7
CPU Instructions
Enabled dual push button / autonomous control
Push button priority control
  Same control implemented for Project 2
Autonomous control when push buttons not used
  Avoid edge of world
  Avoid obstacles (barriers=2, trees=3)
  Follow black line
Added CPU port to handle single long-range sensor
Scripting
Created perl script to generate COE file from BMP image
File combines COE header with BMP bit data

## Slide 8
CPU Instructions Next Steps
Expanding CPU ports to handle new three individual long-range sensors (LRLeft / LRCent / LRRight)
Evaluating quality control of bot actions
Scripting Next Steps
Debug sporadic mis-conversion of BMP2COE pixels

## Slide 9
Verilog
Modified Modules
nexys4fpga.v
nexys_bot_if.v
bot.v
world_if.v
Debugged manually generated COE file for POC
Used project 2 and custom icon to show colors and unique design
Created colorizer module to support 4-bit BMP color scale

## Slide 10
Verilog Modules Next Steps
Expand modules to Include additional sensors (per lane)
All modules
Colorizer2 to handle extra coloring schemes for world vs bot
BMP2COE conversion script verification / debug
Vivado project development
Unique bot design?

## Slide 11
Bot Eye (1024x512)
Wheel icon
(512x512)
World Map
(512x512)
VGA Graphics
Divided 1024 x 1024 display screen into 3 sections
Bot Eye (1024x512)
  Converts bot image size (128x64) to 1024x512
  Uses two images
  Image 1 for orientation = 0/90/180/270
  Image 2 for orientation = 45/135/225/315
Wheel Icon (512x512)
  Converts bot image size (64x64) to 512x512
  Uses two images
  image 3 for orientation = 0/90/180/270
  Image 2 for orientation = 45/135/225/315
World Map (512x512)
  Uses world map for right end corner 512x512

## Slide 12
VGA Graphics Next Steps
Display 1024 x 1024 BMP2COE converted image on screen
Display 512 x 512 World Map image from Project 2 in lower right corner of full display
Display 512 x 512 Control Console (Steering Wheel, etc.) in lower left corner
Add trees (value=3) to world map
Run map file through script to create COE for ROM build
Verify map conversion via display

## Slide 13
End